EM 1 - Corrigé de la partie B de l’examen de janvier 2011

RECYCLING HEAT FROM THE AIR PUMPED OUT OF INTENSIVE PIG HOUSES

Synthèse en français en 15-20 lignes maximum.

| mots-clés en anglais = squelette de la synthèse | points |
| --- | --- |
| intensive pig houses cutting down energy consumption (e.g., insulation, full houses, accurate controls) | 1 |
| + air-to-air heat recovery (ventilation system) : from warm exhaust air to cold supply air efficiency : 70% | 2 |
| method 1 : PHEs (no moving parts ( easy maintenance) warm and cold air through alternate flow channels + [may…] solar collector ( prevents icing up | 2 |
| method 2 : thermosyphon tube / heat pipe (principle) sealed, finned tubes containing refrigerant 1 end = evaporator (in contact with warm air) other end = condenser (in contact with cold air) ( latent heat of cond. transferred condensate return to evaporator : by gravity = thermosyphon tube by capillarity (wick inside tube) = heat pipe (if condenser NOT above evap.) | 2 + 1 |
| method 3 : 2 rock beds (principle) connected to ventilation system alternately heated and cooled one bed heated while other cooled (con : carry-back of dirt) | 2 |
| total (ramené sur 15) | 10 |